## Slide 1: The Case for UHF-Band MU-MIMO
Naren Anand
Ryan E. Guerra
Dr. Edward W. Knightly
MobiCom 2014

## Slide 2: Introduction
0
f
(GHz)
1
2
3
5
6
2.4GHz
UHF
5.8GHz
TVWS are “beachfront property” of the RF Spectrum
– FCC 2010
-x dB/km
-x-10 dB/km
-x-20 dB/km
-x dB
-x-7 dB
-x-33 dB
Oneloa Bay, Maui
Maui – 144 MHz
Houston – 6 MHz
UHF | 
Better Propagation | Limited Spectrum

## Slide 3: Introduction
MU-MIMO: Precoding technique that enables multi-antenna devices to transmit parallel streams
Properties of the UHF band uniquely benefit MU-MIMO transmissions while providing their own challenges
∠
∠
Channel Variability
Receiver Separability
We demonstrate that UHF combined with MU-MIMO can compensate for these challenges and overcome the spectral limitations of the UHF band.

## Slide 4: Outline
MU-MIMO Background
Testbed Design and Integration
OTA Measurements and Analysis

## Slide 5: MU-MIMO Background
MU-MIMO: linear precoding method that allows a multi-antenna AP to transmit multiple parallel data streams to groups of clients
  Precoding: Applying complex magnitude and phase offsets (steering weights) to each data stream through the transmitting antenna array
  Steering Weights: W matrix computation based on measured magnitude and phase offsets for each Tx->Rx antenna path (CSI Matrix)
    e.g., Zero-forcing Beamforming
Tx
Rx B
Rx C
Rx A
Wa·Da
Wb·Db
Wc·Dc
Data-a
Data-b
Data-c

## Slide 6: MU-MIMO Tx Procedure
Two step process:
  SOUND – Measure channel between Tx and Rx antennas
  TRANSMIT – Transmit parallel streams to multiple users
Rx B
Rx C
Rx A
a
b
c
Tx

## Slide 7: MU-MIMO Performance
∠
∠
Channel Variability
Receiver Separability
Two Key Performance-Determining Factors
How much do the users (or their environments) move?
How temporally correlated are the users’ channels?

## Slide 8: Receiver Separability
Rx B
Rx C
Rx A
How close are the users’ channels?
  Linear dependence of H matrix rows
  NOT necessarily dependent on physical location
∠
∠
∠
∠
Tx
∠
∠
UHF?
2.4 GHz
5.8 GHz
?
?
How to Quantify?
Demmel Condition Number
  [35] C. Zhong, et. al. 2011
  Based on Linear dependence
  Thus, invertibility
  Reliably predicts performance
    eg., use for MCS
  [1,∞] : 1 -> perfectly separable (orthogonal) channels

## Slide 9: Channel Variability
Rx B
Rx C
Rx A
b
c
How much do the users (or their environments) move?
  Between SOUNDING and TRANSMISSION
  How “fast” is the user/environment changing?
a
Tx
SOUNDING
TRANSMISSION
and
4.5m/s
1.5m/s
13m/s
λ/s
m/s
UHF
2.4 GHz
5.8 GHz
λ
60cm
12cm
5cm
X
x
5x
12x
2.5
13
30
How to Quantify?
elem(H) autocorrelation
  Measures change of each antenna path
  [0,1] : 1-> identical for given lag
  Rate of decay w.r.t. lag:
    Slow decay, sound less
    Fast Decay, sound more
7.5
38
90
21
108
260
λ/s

## Slide 10: MU-MIMO: UHF vs 2.4/5GHz
MU-MIMO
Channel Models
OTA Characterization
Channel Variability
Receiver Separability
?
?
?
?
5.8 GHz
Indoor
[27] Poutanen 2011
300 MHz
Outdoor
[36] Zhu 2013

## Slide 11: MU-MIMO Channel Models
COST 2100 -> MU-MIMO modelling framework
Parameterized for 300 MHz outdoor and 5 GHz indoor through exhaustive OTA measurements
Models tell us:
  UHF MU-MIMO users are harder to separate than 5GHz
  UHF MU-MIMO channels are less variable than 5GHz
300MHz
5.8GHz
300MHz
5.8GHz
Order of magnitude

## Slide 12: MU-MIMO: UHF vs 2.4/5GHz
MU-MIMO
Channel Models
OTA Characterization
Channel Variability
Receiver Separability
More
Variable
Easier to Separate
Less
Variable
Harder to Separate
More
Variable
Easier to Separate
?
?
5.8 GHz
Indoor
[27] Poutanen 2011
300 MHz
Outdoor
[36] Zhu 2013
2.4/5.8 GHz Indoor
[9] Aryafar 2010
UHF
In/Outdoor
[*] Anand 2014

## Slide 13: Outline
MU-MIMO Background
Testbed Design and Integration
OTA Measurements and Analysis

## Slide 14: WURC Array
How do you build a UHF MU-MIMO array?
Common UHF Antennas are cumbersome -> especially for indoor deployments
40cm
35cm
Log-periodic
50cm
100cm
Sector
45cm
185cm
Ryan
Enterprise AP and
WARP SDR
25cm
12cm
7cm
12cm
Omni
λ/2=30cm
UHF array achieves MU-MIMO gains even with SFF antennas -> Indoor WLAN sized

## Slide 15: WURC Array
Open UHF MU-MIMO development platform
  d
Side by side comparisons of 2.4/5Ghz and UHF band
4 WARP + 4 WURC
Clock and trigger sync. - > coherent transmitter
λ/2=6cm
λ/2=30cm
UHF Antenna
Dual-Band WiFi Antenna

## Slide 16: WURC
High power, Multi-band radio front end
  Custom design - built with LMS6002D
  Up to 1 Watt Tx power with custom PA chain
  Demo: An Open-Source Development Platform for Long-Range UHF-Connected WiFi Hotspots
Digital I/O
µCtlr
Power
dist.
Tx
PA Chain
TRX
Rx
LNA
2.4 GHz
DPDT
Wideband
Rx
UHF
DPDT
Wideband UHF Radio Card
Open
Frequency-Agile
Microsoft SORA
Rice WARP
Nutaq SFF-SDR
Ettus USRP
Nutaq PicoSDR
WURC
Nuand BladeRF
Carlson RuralConnect
Myriad RF
Fairwaves UmTRX
Adaptrum
High Power

## Slide 17: Outline
MU-MIMO Background
Testbed Design and Integration
OTA Measurements and Analysis

## Slide 18: OTA Measurement Methodology
Exhaustively characterize the channel
Zero-forcing Beamformer
  Based on WARPLab design flow
    [9] Aryafar 2010, Shepard 2012, Anand 2012
  MATLAB Centric PHY layer prototyping platform
  Allows for less complex implementation of Zero-forcer
    measure SINR -> Aggregate Shannon Capacity
  High communication latency.
  Topology restricted by cabling.
High speed WARP-based channel sounder
  Based on WARP-802.11 Reference Design
    Allows for MU-MIMO channel sounding
    with a relatively low cost set of SDRs
  LTS for OFDM channel estimation
  Provides high speed channel snapshots
  not actual beamforming

## Slide 19: Indoor Scenario
Typical, challenging Indoor Environment
  Environmental mobility from office
  Industrial building: Concrete and steel propagation environment
  Non-Line of Sight
  Close colocation of receivers
Will UHF propagation allow for user separation?
Does the UHF MU-MIMO channel actually stay stable?
Tx
Rx
Rx
Rx
Rx
Rx
Rx
Walkway
Concrete

## Slide 20: Indoor Scenario
2.4GHz
UHF
5.8GHz
Sum capacity peaks at 4x3
  [9] Aryafar 2010
Propagation of 5.8 GHz diminishes performance
Recall UHF user separability
  Propagation through obstacles should reduce multi-path
Equivalent capacity to 2.4GHz
Increasing Tx Distance would show larger performance gain over 2.4GHz
No spectral efficiency penalty for lower frequency

## Slide 21: Indoor Scenario
Will UHF propagation allow for user separation?
  Previous capacity results confirm
  Verify with Condition Number
  Similar H matrix conditioning yields similar capacity
  Models: Indoor 5.8 GHz and Outdoor UHF
2.4GHz
UHF
5.8GHz
User separability is Environment Dependent, not band dependent

## Slide 22: Indoor Scenario
Does the UHF MU-MIMO channel actually stay stable?
  Successful BF confirms
    Atleast for WARPLab latency
  Verify with Temporal Correlation
  UHF: low channel variability even at 802.11 Beacon Interval
  Models: Indoor 5.8 GHz and Outdoor UHF
2.4GHz
UHF
5.8GHz
Channel variability is band dependent

## Slide 23: Indoor Scenario
Relevance of MU-MIMO channel stability for protocol design
  MU-MIMO provides spectral efficiency
  Setup/overhead for transmission?
  Less channel variability -> less per packet sounding
SOUND
(500us)
TRANSMIT
(1300us)
UHF allows for the gains of MU-MIMO with significantly less protocol overhead

## Slide 24: Conclusion
Design open UHF-MU-MIMO platform for side-by-side comparisons of UHF/2.4GHz/5GHz bands
WURC:
Our experiments confirm that UHF-band MU-MIMO exhibits decreased channel variability; however, they show that user separability is equivalent to 2.4/5GHz.
  Channel Variability-> Band dependent
  User Separability-> Environment dependent
Thus, UHF-MU-MIMO leverages benefits of decreased channel variability (lower sounding rate) without suffering from decreased user separability